## Slide 1: Aircraft Design Advanced Meric Taneri
Radical Aircraft Concepts
Aircraft Design Frameworks
UNICADO
Full and Hybrid Electric Aircraft
Hydrogen Aircraft
Unconventional Configurations
Design Evaluation and Life Cycle Assessment
Fleet and Network, Operations

## Slide 2: Previously on UNICADO
A “quick” rundown of component design cluster
Some information about the Aircraft XML file and configurations
Challenges of Component Design
Component Design
Today is going to be all about design analysis and the convergence loop
Design evaluation will be covered at later lectures throughout the semester.

## Slide 3: Design Analysis and Convergence Loop
Aircraft Concept
Component Design
Weight and Balance Analysis
Mission Performance Requirements
Point Performance Requirements
Constraint Analysis
Mission Analysis
Weight fractions
TLARs
Design Choices
Component Design

## Slide 4: Design Analysis
Analyzes the current state of the design
Where snowball effects and trends are realized
Where assumptions and documentations become crucial
Where robustness becomes an issue
Design Analysis
Component Design
Three objectives:
Capture fundamental phenomena
Allow integration of higher fidelity analysis tools to capture additional effects
Documentation

## Slide 5: Aerodynamic Analysis
Let’s do an example functional breakdown
What do I need from an “aerodynamic analysis” tool?
Design Analysis
Component Design
Calculate
Calculate
Calculate
Calculate
Calculate
Calculate
Calculate
Calculate
Create polar
Store polar
Read A/C geometry
Do trim

## Slide 6: Aerodynamic Analysis
Here is a list of tools and methods that are available for doing Aerodynamic Analysis – some are in UNICADO
UNICADO uses the Lifting Line Version 3.1 developed by Karl Heinz Horstmann
Integration of AVL is in progress
Polhamus (from Aircraft Design Basics) can be integrated
Design Analysis
Component Design
Aerodynamics
XFoil (Drela)
Xrotor (Drela)
PAWAT – propeller and wing aerodynamics tool (in-house: Steiner)
AVL (Drela)
Lift curve slope calculation (Polhamus, slender body, lifting line, Ackeret)
Drag component build-up method (Raymer)
Equivalent skin friction method (Raymer)
Transsonic wave drag increase estimation (Malone & Mason)
Oswald factor estimation (Nita & Scholz)

## Slide 7: Aerodynamic Analysis
Lifting_Line – Assumptions
    Potential-theoretical procedure for the case of a
        smooth,
        incompressible flows,
        assuming that the airfoil profiles are thin and able to be modelled by flat plates
    An inviscid, irrotational and steady flow around a wing is modeled by the distribution of a system of singularities over the wing and the superposition of this system with the undisturbed incoming flow
    If necessary, a compressibility correction (Göthert) with the appropriate geometric modifications can be switched on
Vortex Lattice (AVL) – Assumptions
    Best suited for aerodynamic configurations which consist mainly of:
        thin lifting surfaces
        at small angles of attack
        at small angles of sideslip
    Assumes quasi-steady flow, meaning that unsteady vorticity shedding is neglected.
    Compressibility is treated in AVL using the classical Prandtl-Glauert (PG) transformation

## Slide 8: Aerodynamic Analysis
Questions:
Are the assumptions checked?
    They should be checked
What if the configuration does not comply with the assumptions
    Throw a warning message to inform the user or,
    Create an internal procedure to make the correction
        Do not make the correction to get to a number, make the correction to get the phenomena
Can all the functions be fulfilled with just AVL or Lifting_Line?

## Slide 9: Aerodynamic Analysis
What does Lifting_Line give us?
of the lifting surfaces under the following limitations
      Linearization and the neglect of the viscous properties
      Göthert incorporates only the effects of pure subsonic flows around thin airfoils
      Transonic speed range lead to increasing in-accuracy here
We need another method than the one implemented in Lifting_Line to capture compressibility and we still need to get of the aircraft
Transsonic wave drag increase estimation (Malone & Mason)
Drag component build-up method (Raymer)
Compressibility: Prandtl-Glauert transformation
Trim with linear interpolation
Design Analysis
Component Design
Notes: Mention that the documentation can be given if wanted

## Slide 10: Aerodynamic Analysis
Component Build-up Method from Aircraft Design Basics: Is applied within the design environment
Why? Because you can get the trends and snowball effects even with these “very simple” equations
+ You can use these methods on “segments” rather than the whole surface to make them more “complex”

## Slide 11: Aerodynamic Analysis
Main challenge
Capturing assumptions and conditions under which the equations and methods are applied
In UNICADO aerodynamic analysis, there is a “one method to rule them all” approach meaning that a single method is implemented and applied to all conditions and configurations without any documentation
A good documentation example would be USAF STABILITY AND CONTROL, DATCOM ADB072483
      3134 pages of pure documentation
Always make sure to check the assumptions and limitations of tools that you implement
Make sure to document these for the users
Add references to the material that you are using

## Slide 12
Source: R. D. Finck, USAF STABILITY AND CONTROL DATCOM, McDonnell Douglas Corporation Douglas Aircraft Division, 1978, Section 1, 1-7
Notes: There is a lot of room to grow in UNICADO
This report is a collection, correlation, codification, and recording of best knowledge, opinion, and judgment in the area of aerodynamic stability and control prediction methods. It presents substantiated techniques for use 1 early in the design or concept study phase, 2 to evaluate changes resulting from proposed engineering fixes, and 3 as a training on cross-training aid. It bridges the gap between theory and practice by including a combination of pertinent discussion and proven practical methods. For any given configuration and flight condition, a complete set of stability and control derivatives can be determined without resort to outside information. A spectrum of methods is presented, ranging from very simple and easily applied techniques to quite accurate and thorough procedures. Comparatively simple methods are presented in complete form, while the more complex methods are often handled by reference to separate treatments. Tables which compare calculated results with test data provide indications of method accuracy. Extensive references to related material are also included.
Final rept. Sep 1975-Sep 1977

## Slide 13: Mission Analysis
Mission Performance Requirements
Mission Analysis
Weight fractions
Component Design
Design Analysis

## Slide 14: Mission Analysis
Challenges of Mission Analysis
The mission analysis shall create a mission from Top Level Aircraft Requirements and Mission Requirements
        The mission profile might not be given in some cases
        A design mission that fits the requirements must be automatically generated to get the mass properties of the aircraft
Putting mission analysis in a convergence loop comes with additional challenges
        The convergence loop requires the mass properties in each iteration
        This means that the tool must be able to handle “infeasible” configurations
        The tool must also provide enough complexity to capture the snowball effects
Increased granularity and doing optimization comes with increased runtime
Mission Analysis

## Slide 15: Mission Analysis
There are two Mission Analysis tools in UNICADO which take two approaches
DEFAULT Approach
Mission is created in detail based on the TLARs and Mission Requirements
Operating conditions and flight conditions are calculated at each step of the segment
Changes the conditions iteratively until the required end conditions of the steps are reached
Possible segments:
takeoff
climb
climb_to_cruise
climb_to_ceiling
change_flight_level_constant_ROC
accelerate
change_speed
change_speed_to_CAS
change_speed_to_Mach
cruise
descend_to_approach
descend
level_glide_slope_interception
landing

## Slide 16: Mission Analysis
Δh
What happens if the aircraft does not have enough Specific Excess Power at the current iteration?
It gets stuck in the loop
This mode assumes that the aircraft CAN FULFILL all requirements

## Slide 17: Mission Analysis
The default approach has some neat functionality like flight path optimization
BUT
If the aircraft is in the loop, and if the current state of the aircraft is not meeting the requirements, this tool aborts execution
Without a mass estimation, the convergence loop fails
This tool does not work while the aircraft is moving in the design space
Mission Performance Requirements
Mission Analysis
Weight fractions

## Slide 18: Simple Mission Analysis
We need a second approach that is robust enough for the convergence loop to continue execution
Garbage in – garbage out, but you still get something out
Fast execution – no iterations unless necessary
Very simple, decision tree based approach for going from one state to another
Input Format
Check-Point to Check-Point
Segment Definition
1
Altitude
Mach
Distance or time
2
Altitude
Mach
Distance or time
Use Case: Setting up pre-defined climb or descend profiles
Flight profile dictates the analysis
1
2
Altitude
Mach
Altitude
Mach
Distance
Use Case: Simple segment definitions from top level requirements
Aircraft characteristics dictate the analysis

## Slide 19: Simple Mission Analysis
Basics
The decision tree is based on the Energy Height concept
Any combination of acceleration and altitude change can be evaluated with a simple logic
1
2
h_1
M_1
R_1
h_2
M_2
R_2
Start
Target
i
h_i
M_i
R_i
i-1
i-2
…
…
…
2
1
0
State i
State vector
where is the total change in energy height

## Slide 20: Simple Mission Analysis
Decision Tree – State Transition
Cruise
50% SEP  Climb
50% SEP  Acceleration
100% SEP  Acceleration
100% SEP  Climb
Accelerated Climb
Accelerated Climb
Accelerated Climb

## Slide 21: Simple Mission Analysis
Decision Tree – State Transition
Cruise
Set linear flight path
2
Calculate
Calculate with remaining SEP
Decelerated descent
Calculate with SEP
Calculate with SEP
Decelerate
Descend

## Slide 22: Simple Mission Analysis
Fail Cases
What if the aircraft does not have enough thrust to increase its energy state?
      Means that the aircraft is not meeting the point performance requirements – not my tool not my business
      The loop still needs the mass properties to continue
          Put thrust to more than 100%?
          Stop climbing and continue from that altitude?
What if the fuel tanks are empty?
      We work with mass fractions – fuel tanks are only used for shifting the cg
          Use the final location of the cg for trimming
What if the aircraft does not have enough drag to decrease its energy state?
      This is rather a problem of setting up the descent profile
          Move the “transition point” backwards
2
1

## Slide 23: Constraint Analysis
Point Performance Requirements
Constraint Analysis
Weight fractions
Component Design
Design Analysis

## Slide 24: Constraint Analysis
Energy Based Constraint Analysis
Point performance requirements are evaluated as constraints within the , design space
Energy based formulation approach taken from Mattingly, J., D., Aircraft Engine Design
Can be configured to:
      Select the min and corresponding
      Select the min that is corresponding to a constant
      Keep both , constant and perform a requirement check

## Slide 25: Constraint Analysis
Energy Based Constraint Analysis
Multiple cases can be evaluated using the functions provided in the constraint analysis module
The Constraint Analysis config file can be used to add additional point performance limitations to the ones coming from the TLARs
Possible Constraints
Cruise Mach number
Constant speed climb
Constant altitude/speed turn
Horizontal acceleration – dash
Takeoff ground roll
Braking roll
Service ceiling – SEP
Takeoff climb angle
Gust

## Slide 26: Constraint Analysis
Initialize
For each case:
Read polar
Get CD
Evaluate constraint
Find Dominant Curve
Find minimum
Find corresponding
Update design point

## Slide 27: Constraint Analysis
Challenge of Constraint Analysis and Convergence Loop
The constraint analysis module (or constraint sizing module) selects a new design point based on the point performance requirements
If the selection method is not constructed carefully, it might result in oscillations in the design point
      These oscillations can prevent convergence
If the design tools cannot handle movement within the design space, selecting a new design point can halt execution
      But is this the fault of constraint analysis, or the design tools?
Chart: Number of Iterations
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9
W/S | 572 | 549 | 531 | 521 | 517 | 514 | 514 | 513 | 513
T_SL/W_TO | 0.4848 | 0.4581 | 0.4373 | 0.4271 | 0.4226 | 0.4209 | 0.42 | 0.4201 | 0.4201

## Slide 28: Convergence Loop
Aircraft Concept
Component Design
Weight and Balance Analysis
Mission Performance Requirements
Point Performance Requirements
Constraint Analysis
Mission Analysis
Weight fractions
TLARs
Design Choices
Component Design

## Slide 29: Convergence Loop
Converged Aircraft
The aircraft that meets all the
      Top Level Aircraft Requirements
      Mission requirements
      Performance requirements
The aircraft configuration that does not change through iterations
      For parameter P:
What could be a parameter of interest for convergence?
      Mass properties: ?
      Design point: ?
      Center of gravity position?
Chart: Number of Iterations
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17
W/S | 572 | 549 | 531 | 521 | 517 | 514 | 514 | 513 | 513 | 513 | 513 | 513 | 513 | 513 | 513 | 513 | 513
T_SL/W_TO | 0.4848 | 0.4581 | 0.4373 | 0.4271 | 0.4226 | 0.4209 | 0.42 | 0.4201 | 0.4201 | 0.4201 | 0.4201 | 0.4201 | 0.4201 | 0.4201 | 0.4201 | 0.4201 | 0.42011
Choose the convergence criteria wisely, you might get stuck in iterations

## Slide 30: UNICADO in RCE
Component Design